NEC Solutions America Inc.

2355 Gold Meadow Way, Suite 200

Gold River, California 95670

Telephone (916) 463-7000

Fax (916) 463-7041

Live Scan to NEC GTC

Interface Specification

Texas Special and NIST

Type 2 Definitions

November 21, 2007

Appendix B —  Livescan to NEC GTC Interface Specification	1

B.1 	SCOPE	1

B.2 	REFERENCED DOCUMENTS	2

B.3 	STANDARDS TO BE USED	2

B.4 	GENERAL TRANSMISSION REQUIREMENTS	4

B.5 	DATA TRANSFER USING FTP	6

B.6 	GTC DIRECTORY STRUCTURES	7

Common Directory Layout	7

Submission Directory Layout	8

B.7 	SUBMITTING TEXT AND IMAGES	10

The Procedure	10

Text and Image Set File Name	11

Signal File Name	11

Return Message File Names	12

B.8 	FILE FORMATS	12

Tag/Value File Format	12

Signal File	12

Acknowledgment File	13

Return Message Formats	13

B.9 	FILE DEFINITIONS	18

LS Configuration File	18

Validation Revision Control File	18

B.10 	MESSAGE CODE TABLES	19

Administrative Response Code– TABLE 11.1	19

Accept Response Code - TABLE 11.2	19

Reject Response Code - TABLE 11.3	20

B.11 	MESSAGE EXAMPLES	21

Administrative Messages	21

Acknowledgement Messages	21

Reject Messages	22

Identification Response Messages	24

Non-critical Error Messages	25

Signal File (new submission)	27

LS Configuration File	27

Validation Revision Control File	27

Tag 2.067 Examples	28

Appendix C — NIST Type 2 Definitions	1

ER2 NOTES:	4

ER4 NOTES:	4

ER5 NOTES:	4

# Appendix B — 
Livescan to NEC GTC Interface Specification

## B.1 	SCOPE

#### Identification

This document applies to all devices submitting fingerprint and Palm images and associated demographic data to the NEC Global Transaction Controller at the Texas DPS using the Livescan interface.  This version is an adaptation of the Livescan to NEC GTC Interface Specification (Revision 3.0) and is specific to the GTC at the Texas DPS.  The additional features in this document are not necessarily available with other implementations and for the most part deal with the Texas Electronic Arrest Reporting (EAR) requirements and the unique data set required by that program.

This document contains specifications that govern how devices will submit fingerprint and text data to the NEC GTC.  The discussion is limited to software and procedural considerations.

The changes made to the Livescan to NEC NATMS Interface Specification (Revision 3.1T) to produce this document do not affect the data submitted but deal primarily with message return (GTC to LS) formats, methodology and content.

#### Revision History

- 1996	Version 1.0

- April 10, 1997	Revision 2.0

- June 22, 1998	Revision 3.0.  Updated to allow FTP as a transmission protocol.

- October 26, 1998	Revision 3.1T Document specific to TCHIP project in Texas.

- October 3, 2003	Revision 3.2    Updated for GTC/NATMS project

## B.2 	REFERENCED DOCUMENTS

For a complete picture of the context in which this system is to operate please see the latest revision of the following documents

- Texas DPS GTC Phase I Technical System Design, July 2004

- Texas DPS Computerized Criminal History (CCH) Data Dictionary (October 6,1998)

- Texas SB41 Chapter 60 Enhanced Computerized Criminal History (CCH) Remote Terminal Interface Using LU6.2 Transaction (SNA SDLC) (November 22, 1995)  SEE Note:

- ANSI, Data Format for the Interchange of Fingerprint Information (ANSI/NIST-ITL-2000)

- Electronic Fingerprint Transmission Specification (EFTS), which includes Appendix F, IAFIS Image Quality Specifications (CJIS-RS-0010v7).

Wavelet Scalar Quantization (WSQ) Gray Scale Fingerprint Image Compression Specification (IAFIS-IC-011v2 February 16, 1993)

NOTE:  The use of this specification is for the definition of data formats and does not express the intent of NEC to support LU6.2 or SNA SDLC.

## B.3 	STANDARDS TO BE USED

Livescan systems must comply with the FBI’s Integrated Automated Fingerprint Identification System (IAFIS) Image Quality Specifications (IQS).  IAFIS is developed according to standards that establish an infrastructure for the exchange of fingerprint identification information between local, state and federal users, and between those users and the FBI.  To exchange fingerprint identification data effectively across jurisdictional lines or between dissimilar systems made by different manufacturers, standards are needed to specify a common format for the data exchange.  Therefore, Livescan devices are required to meet the FBI’s IAFIS standards and those amended by NEC’s Customer to include the following specifications.

#### The American National Standard Institute (ANSI) Standard, Data Format for the Interchange of Fingerprint Information (ANSI/NIST-ITL 2000)

This standard defines the content, format and units of measurement for the exchange of information that may be used in the fingerprint identification of a subject.  Such information is intended for use in the interchange between criminal justice administrations or organizations that use an Automated Fingerprint Identification System (AFIS), and will provide a common interface for AFIS systems and related systems nationwide.

#### Electronic Fingerprint Transmission Specification (EFTS), Which Includes Appendix F, IAFIS Image Quality Specifications (CJIS-RS-0010v7)

This document specifies the file and record content, format, and data codes necessary for the exchange of fingerprint identification information between Federal, local and State users and the FBI.  It provides a description of all requests and responses associated with electronic fingerprint identification services.  It also establishes error messages, specific compression algorithms for the exchange of fingerprint image information, and image quality assurance methods.  Appendix A establishes the priorities of incoming transactions.  Appendix B includes field edit specifications and a sample Logical Record Layout for the Type 1 record.  Appendix C is the Descriptors and Field Edit Specifications for the Type 2 records.  Appendix D includes Type 2 record samples of each Latent and Image Type of Transaction.  The Logical Record Layouts in Appendix D and E include the following:

- TOT

- Message identifier

- Condition (optional or mandatory field)

- Field number

- Field name

- Character type (alpha, numeric, special characters)

- Field size per occurrence (minimum and 	maximum)

- Number of occurrences allowed (minimum and maximum)

- Total bytes allowed per field

- Example data for each field

A special characters list for each field

Appendix F applies to fingerprint scanner systems and printers that will supply fingerprint data to the Integrated Automated Fingerprint Identification System (IAFIS), and to printers and displays within the IAFIS. They provide objective criteria for insuring image quality. The scanner shall capture fingerprints at a minimum resolution in both the detector row and detector column directions (also know as ‘along - scan’ and ‘cross - scan’ directions) of 500 pixels per inch, plus or minus 5 pixels per inch.  The final output image delivered from the scanner system shall have a resolution of 500 pixels per inch, plus or minus 5 pixels per inch, and each pixel shall be gray level quantized to 8 bits.

#### The WAVELET Scalar Quantization (WSQ) Gray Scale Fingerprint Image Compression Specification (IAFIS - IC - 0110v2 February 16, 1993).

This standard specifies a class of encoders for converting source fingerprint image data to compressed image data, a decoder process for converting compressed image data to reconstructed fingerprint image data, and coded representations for compressed image data.

Every image electronically submitted to the state must be compressed using the WAVELET Scalar Quantization Compression Algorithm.  This algorithm consists of a class of encoders for converting source fingerprint image data to compressed image data, a decoder process for converting compressed image data to reconstructed fingerprint image data, and coded representations for compressed image data.

The WSQ compression algorithm was selected for it’s compatibility with fingerprint data and GTC will not accept uncompressed electronic images.  The compression rate for fingerprint images will be 15:1.  However, GTC will accept electronic images captured with a compression rate of 5:1 for those devices certified at the Minimum Image Quality Requirement level established by the FBI.

## B.4 	GENERAL TRANSMISSION REQUIREMENTS

Each Livescan device will submit National Institute of Standards and Technology (NIST) format text and images to the NEC GTC using either the Network File System (NFS) protocol or the File Transfer Protocol (FTP).  Before a Livescan device can connect to the GTC it will be provided with the following data items:

- Device ID

- Group ID

- Password (NFS only)

- TCP/IP address

- Name of the Host to access

The name of the “common” directory to access

The Device ID will be a three-character device identifier that will be unique for each Livescan device.  This device id must be used in all submissions to the GTC.

The Livescan device will also be assigned to a logical group designated by the Group ID.  The group id will be four characters in length and will be associated with the submission directory.

The common directory will contain the latest versions of data validation tables and environmental information that will tell Livescan devices which directories to write their submissions to.

The environmental information will specify the name of another directory called the submission directory that will be used to receive submissions from the network.

There will be only one common directory but there will be at least one submission directory.  The actual number of submission directories is determined by the system administrators.

When these data items are obtained, the Livescan device will use the following general procedure each time it initially connects to the network:

- Access the common partition.

- Verify that it has the latest versions of validation tables by examining files found in the common directory. See Note 1

- Update tables on the Livescan that are out-of-date using files found in the common directory. See Note 1

- Read an “environment” file in the common directory that contains the name of another directory (the submission directory) to which submissions will be sent.

- Access the submission directory named in the environment file.

For each submission the Livescan device will:

- Write the NIST data to the Livescan device id directory in the submission directory.

Write a signal file to the signal file directory in the submission directory.

After the GTC has recognized the submission and assigned a control number to it, the control number will be made available to the Livescan device.

Copies of tables used by the Livescan device to validate text data prior to submission will be made available in the common directory.  It is the responsibility of the Livescan device to examine the directory containing these tables and insure that the latest versions are downloaded.  The Livescan device will copy new tables from the common directory as needed.  See “Common Directory Layout” and “Validation Revision Control File” later in this document for details.  See Note 1

After AFIS processing is complete, the GTC will make available to the Livescan device the return message.  See B.9.4 “Return Message Formats” for message details.

Note 1:  This specification governs the NEC GTC functionality.  Early Livescan implementations may not have the functionality to download validation tables.  The capabilities of each are governed by the agreements under which those procurements were made.

## B.5 	DATA TRANSFER USING FTP

GTC also supports data transfer by means of anonymous FTP.  In this protocol the livescan device connects to GTC through an FTP client with the user id “anonymous” and “anonymous” as the password.  Once a session has been established the livescan device should change to the pub directory.

The common directory will be in the pub directory under the name lscommon.  This directory will have the same structure and content as the one used for NFS protocol.

The environment files in the FTP common directory will all specify the pub directory as the submission directory.  Thus a typical environment file would be similar to

pub,1,1

This implies that the pub directory will contain, besides the common directory, a signal files directory and several group directories.  For example, a directory listing of the pub directory might show lscommon and sigfiles along with directories for each of the livescan groups using FTP.

The exact structure of these directories is described in Section B.7.

The Livescan is responsible to poll its out directory and the GTC will perform basic housekeeping functions.

## B.6 	GTC DIRECTORY STRUCTURES

### Common Directory Layout

The common directory will contain two sub-directories.  The first, called envfiles, will contain a LS Configuration File for each group of Livescan devices.  The second sub-directory, called valtabs, will contain the latest validation tables once implemented.

The LS Configuration File will contain one line of text that will be the name of the directory to which the devices in the group will write submissions.  All of these files will be kept in a directory called envfiles.  The name of the file will be the group id assigned to the Livescan device.

For example, a Livescan device assigned to group grp1 will open and read the contents of the LS Configuration File called envfiles/grp1.  The first line of the file will contain, beginning in column one, the name of the directory to which the device will write its submissions. (Also, the file will contain the interval timer and the maximum amount of time to check the out directory for the message back from GTC.)

Permissions on these files will be such that the Livescan device will have access only to its own file.  The purpose of these environmental files is to allow the GTC system administrator to manage the distribution of disk space usage in the submission directories.  The Livescan device must read its environment file when it first connects to the network.  The Livescan device administrator will be notified in advance of any changes to the directory names.

The valtabs directory, once implemented, will contain a copy of each validation table and a control file that will contain the implementation date of the latest version of each validation table.  The validation tables and the control file will all be stored as flat files with one line of text per entry.

The control file will be called revcon.dta.  It will contain a header record consisting of an eleven (11) character current table set version number.  This will be implementation date and time of the table set (always a past date).

Following the header record will be one line of text for each validation table.  Each line will start with an eleven (11) character table version number consisting of the year, date, and time of implementation (always a past date) of the table and the name of the table beginning in column twelve (12).  Each Livescan device will be responsible for ensuring that it is using the latest version of each table. The year will be 0000-9999, the date will be in Julian (001-366) format, and the time will be in hours and minutes based on a 24-hour clock.

The revcon.dta table should be checked at the Livescan each time an operator logs on.

Following is an example of the common directory structure. Each implementation may have its specific set of validation tables.

| Directory/File Name | Directory/File Description |
| --- | --- |
| lscommon | Name of the common directory |
| envfiles | Directory containing assignment files |
| grp1 | LS Configuration File for devices in group grp1 |
| nc01 | LS Configuration File for devices in group nc01 |
|  | More group environment files |
| valtabs | Directory containing current validation tables |
| revcon.dta | Version control file |
| ori.tbl | Current ORI table |
| ofc.tbl | Current Offense Code table |
| … | Remaining tables as added |

### Submission Directory Layout

Each submission directory area will have a sub-directory for each group assigned to that area and a sub-directory called sigfiles where the Livescan devices in the assigned groups will write their signal files.

For the example below, the submission directory /home/natms/tc/lsdir/nfs (as specified in the LS configuration file, see section 10) containing groups def3 and rs7 will have the following sub-directories:

- def3

- rst7

sigfiles

The name of the group directory will be the same as the group name.  Each group directory will have one sub-directory for each Livescan device assigned to that group.  The name of these device sub-directories will be the same as the Livescan device ids.

Finally each device sub-directory will have beneath it a single sub-directory called out.  The out directory will be used to find the SUBMIT file and an acknowledgment file from GTC.  (This is discussed in more detail further on).

Suppose, then, that Livescan devices abc and 123 are assigned to group def3 and that Livescan device jkl is assigned to group rst7.  The full directory structure would be:

| Directory Name | Directory Description |
| --- | --- |
| /home/natms/tc/lsdir/nfs/def3/abc | NIST text and image directory assigned to Livescan device abc group def3 |
| /home/natms/tc/lsdir/nfs/def3/abc/out | SUBMIT, return message and acknowledgment file directory assigned to Livescan device abc group def3 |
| /home/natms/tc/lsdir/nfs/def3/123 | NIST text and image directory assigned to Livescan device 123 in group def3 |
| /home/natms/tc/lsdir/nfs/def3/123/out | SUBMIT, return message and acknowledgment file directory assigned to Livescan device 123 group def3 |
| /home/natms/tc/lsdir/nfs/rst7/jkl | NIST text and image directory assigned to Livescan device jkl in group rst7 |
| /home/natms/tc/lsdir/nfs/rst7/jkl/out | SUBMIT, return message and acknowledgment file directory assigned to Livescan device jkl group rst7 |
| /home/natms/tc/lsdir/nfs/sigfiles | directory where Livescan devices abc, 123 and jkl will write their signal files |

(For anonymous FTP, /home/natms/tc/lsdir/nfs, the submission directory, would be replaced by pub.)

In the event that the submitting device is a Livescan store and forward concentrator with multiple Livescan devices underneath, a group id will be assigned to that concentrator.  The concentrator’s individual Livescan devices will be the only device sub-directories contained within that group id.  Submitting of NIST text and image data will be the same as below, noting that the Livescan store and forward must write the data to the proper Livescan device sub-directory associated with the submission.

## B.7 	SUBMITTING TEXT AND IMAGES

### The Procedure

Each time a Livescan device has a NIST record to send it will check the out directory for the presence of a file named SUBMIT. The presence of this file indicates that the Livescan may submit NIST records to GTC.  The absence of this file indicates that Livescan may not submit NIST records.  If Livescan submits NIST records without the SUBMIT file being present, the submissions will be ignored by GTC.

When the SUBMIT file is detected, the Livescan device will copy the text and image set to the GTC in the appropriate submission directory.  The text and image set will be concatenated into a single file.  The file name of the text and image set must be in the format of ddhhmmss to distinguish it from previously submitted records.  After transmission of text and images is complete, the Livescan device will copy a signal file to the appropriate sigfiles directory using a name in the format ddhhmmss.LLL where LLL is the Livescan device id.

Once GTC has received a transaction it will write an acknowledgment file (ddhhmmss.LLL) to the out directory indicating the record has been received.  Livescan will check the out directory at a constant interval for an acknowledgment file  If the acknowledgment does not appear in the out directory after a maximum retry count, the Livescan will resubmit the same NIST data again beginning with the SUBMIT check and the generation of a new ddhhmmss file. The time stamp ddhhmmss must be updated and a new signal file generated.

The Livescan will also check the out directory for return messages which will be made available to the Livescan upon completion of AFIS processing or error conditions.

It will be the responsibility of GTC to process and clean up any of these “orphaned” signal files and submission files. The constant interval and the maximum retry count are defined in the LS configuration file in the envfile directory. All text and image data will be submitted in NIST format.

### Text and Image Set File Name

At the time of submission, the device will create within its assigned device directory a NIST file using a name composed of the date and time of the submission. The format will be:

ddhhmmss

where…

| dd | is the current day of the month |
| --- | --- |
| hh | is the hour based on the 24-hour clock |
| mm | is the minutes |
| ss | is the seconds |

### Signal File Name

When transmission of the text and image set is complete, the device will create a signal file in the sigfiles directory using a name composed of the time stamp of the submission and the Livescan device id. The name of the signal file will be in the following format:

ddhhmmss.LLL

where…

| ddhhmmss | is the name of the submission file based on the date/time |
| --- | --- |
| LLL | is the Livescan device identifier |

### Return Message File Names

The return message filenames will be comprised of the three-letter message type (mad, mac, mrj, mid, or mnc) followed by the date and time in ddhhmmss format with the three-digit lsid as the extension. See the following format:

xxxddhhmmss.LLL

where…

| xxx | is the message type |
| --- | --- |
| ddhhmmss | is the date/timestamp |
| LLL | is the Livescan device identifier |

For example, a “mid” message from Livescan id 024 on the 26th at one second before midnight would look like:

mid26235959.024

## B.8 	FILE FORMATS

### Tag/Value File Format

The signal file and the acknowledgment file utilize a tag/value format.  This means that each line is composed of a tag, a colon and a value with no spaces around the colon.  In general the lines may appear in any order.  The last line in a file using the tag/value format must be an end of file marker designated here as “__END__.”  The Livescan device will not honor any file in the out directory that does not have the __END__ marker present. (Note that __END__ has double under-bar in both sides.)

### Signal File

The signal file is created by the Livescan device to indicate that a NIST record is available for processing by GTC.  It will contain the following lines:

SIGF:	ddhhmmss.LLL

__END__

where…

| SIGF | is the tag for a signal file name |
| --- | --- |
| __END__ | is the end of file marker |

### Acknowledgment File

The Acknowledgment file is created by GTC to indicate that it has received the submission.  It contains the following:

SIGF:	ddhhmmss.LLL

ARV:	ddhhmmss

SAN:	nnnnnnnnnn

__END__

where…

| SIGF | is the tag for the signal file name which LS assigned when it submitted the NIST data to GTC |
| --- | --- |
| ARV | is the tag for the arrival time (ddhhmmss) |
| SAN | is the tag for a unique GTC assigned acknowledgement number |
| __END__ | is the end of file marker |

Note:  The contents of the acknowledgment file generated by GTC corresponding to a submission will include all information in the signal file that the Livescan generated (minus the end of file marker) with the ARV and SAN data elements appended to the end.

### Return Message Formats

All GTC to Livescan return messages are a text message starting with a header composed of the following:

- TO

- FROM

- SUBJECT

- DATE/TIME

and a formatted text message. The message will contain identifying data items and possibly appended data, also as formatted text. The message types for the TCHIP project in Texas are as follows:

- ADMINISTRATIVE   (mad)

- ACKNOWLEDGMENT   (mac)

- REJECT   (mrj)

- IDENTIFICATION   (mid)

- NON-CRITICAL ERROR   (mnc)

Provided below are the formats of the message layouts for both the header and text message portions:

#### Header Format (First four lines of each message)

| Line | Description |
| --- | --- |
| TO: | User ID assigned to each Livescan |
| FROM: | NEC GTC |
| SUBJECT: | mad, mac, mrj, mid, or mnc |
| DATE/TIME: | YYYY/MM/DD HH:MM:SS |

#### Administrative Message Format

| Line | Description |
| --- | --- |
| TYPE: | mad |
| CODE: | Administrative code numeric (see table 11.1) |
| LITERAL: | Matches description of code numeric (see table 11.1) |

#### Acknowledgement Message Format

| Line | Description |
| --- | --- |
| TYPE: | mac |
| TCN: | Livescan TCN number |
| SAN: | Unique GTC assigned Submission Acknowledgement Number |
| CODE: | Acknowledgement code numeric (see table 11.2) |
| LITERAL: | Matches description of code numeric (see table 11.2) |

#### Reject Message Format

Reject for all but R300 code critical error

| Line | Description |
| --- | --- |
| TYPE: | mrj |
| TCN: | Livescan TCN number |
| SAN: | Unique GTC assigned Submission Acknowledgement Number |
| TRN: | Locally assigned transaction number |
| RCODE: | Return code numeric (see table 11.3) |
| RLITERAL: | Translation (see table 11.3) |

Reject for R300 code critical error

| Line | Description |
| --- | --- |
| TYPE: | mrj |
| TCN: | Livescan TCN number |
| SAN: | Unique GTC assigned Submission Acknowledgement Number |
| RCODE: | Return code numeric, in this case “R300” (see table 11.3) |
| RLITERAL: | Translation, in this case “Critical Error” (see table 11.3) |
| TRN: | Locally assigned transaction number |
| OCA: | Originating Agency Case Number |
| NAM: | Master name of subject |
| MSG: | A multiple-line message in formatted text, each line preceded by this tag: This is intended as an operator readable message for display (see section B.12 for detailed examples) |
| SEG: | The EAR segment in error is included |

Note:  One or more MSG/SEG groupings may be included.  There will be one MSG/SEG grouping for each EAR file segment (EH, EHN or ER2), which is in error.

#### Identification Response Format

Response for HIT

| Line | Description |
| --- | --- |
| TYPE: | mid |
| TCN: | Livescan TCN number |
| SAN: | Unique GTC assigned Submission Acknowledgement Number |
| SID: | State Identification number |
| AGN: | Local agency assigned identification number |
| TRN: | Locally assigned transaction number |
| OCA: | Originating Agency Case Number |
| NAM: | Master name |
| FBI: | Federal Identification number assigned by FBI |
| FLG: | Blank for HIT response |
| HNH: | HIT or NOHIT (HIT in this case) |
| MSG: | A multiple-line message in formatted text, each line preceded by this tag: Intended as an operator readable message for display (see section B.12 for detailed examples) |

Response for NOHIT

| Line | Description |
| --- | --- |
| TYPE: | mid |
| TCN: | Livescan TCN number |
| SAN: | Unique GTC assigned Submission Acknowledgement Number |
| SID: | State Identification number |
| AGN: | Local agency assigned identification number |
| TRN: | Locally assigned transaction number |
| OCA: | Originating Agency Case Number |
| NAM: | Master name |
| FLG: | * for NOHIT response |
| HNH: | HIT or NOHIT (NOHIT in this case) |
| MSG: | A multiple-line message in formatted text, each line preceded by this tag: Intended as an operator readable message for display (see section B.12 for detailed examples) |

#### Non-critical Error Return (Corrected at DPS - Austin)

| Line | Description |
| --- | --- |
| TYPE: | mnc |
| TCN: | Livescan TCN number |
| SAN: | Unique GTC assigned Submission Acknowledgement Number |
| SID: | State Identification number |
| TRN: | Locally assigned transaction number |
| OCA: | Originating Agency Case Number |
| NAM: | Master name of subject |
| MSG: | A multiple-line message in formatted text, each line preceded by this tag: Intended as an operator readable message for display (see section B.12 for detailed examples) |
| SEG: | The EAR segment in error is included |
| SGC: | The corrected EAR segment is displayed |

Note:  One or more MSG/SEG/SGC groupings may be included.  There will be one MSG/SEG/SCG grouping for each EAR file segment (EH, EHN or ER2), which is in error.  The corrections displayed are applied; resubmission is not required and will cause a duplicate TCN error.

#### Flow Control Message Formats

Administrative messages are intended to control the Livescan NIST submission data flow. These flow control messages will be delivered in the Livescans /out directory detailing the condition in the form described in section 2.6.3.2.

The reactions of the Livescan devices for each type of flow control message are defined in the following table:

| GTC Message | GTC Situation | Livescan Will | Return to Normal Message Expected | Livescan Will Then |
| --- | --- | --- | --- | --- |
| TYPE: ‘mad’ CODE: A050 or A020 Out/SUBMIT file removed. | GTC queue is full. No more NIST submissions can be received. | Stop Transmissions | TYPE: ‘mad’ CODE: A000 Out/SUBMIT file added. | Resume normal transmissions |
| TYPE: ‘mad’ CODE: A010 | GTC queue is approaching full. | Slow down transmissions. Livescan will increase its out file check interval. | TYPE: ‘mad’ CODE: A000 | Resume normal transmission rate |
| TYPE: ‘mad’ CODE: A090 Out/SUBMIT file removed | GTC is shutting down | Stop transmissions | TYPE: ‘mad’ CODE: A000 Out/SUBMIT file added | Resume normal transmissions |

## B.9 	FILE DEFINITIONS

Listed below are the various definitions of files that will interact with the Livescan device.  The order listed is the order encountered.

### LS Configuration File

The LS Configuration File is a control file that contains data items that the Livescan device needs to complete the connection to the GTC.  This file will contain the name of the partition to which a Livescan device will write its submissions.  Also contained will be interval and maximum timer values for the purpose of checking for messages from the GTC. The LS configuration file will contain only a single line with the data fields separated by commas and terminated with a new line character.  There will be one file for each Livescan group.

| File name | /(common partition)/envfiles/(livescan group id) |
| --- | --- |
| Contents | NFS Submission Partition, Interval Timer (minutes), Maximum Timer (minutes) |
| Sample file | /home/natms/tc/lsdir/nfs,1,10 |

### Validation Revision Control File

The Validation Revision Control File contains the version number and implementation date of each validation table in the valtabs directory.  As validation tables are to be updated, the date at which the file was replaced in the /(common partition)/valtabs directory will be entered into this file. The control file will be called revcon.dta.  It will contain a header record consisting of the implementation date and time of the table set (always a past date).  The following lines will contain one line for each validation table.

Each line will start with a table version number consisting of the year (yyyy), date (Julian), and time (hhmm) of implementation (always a past date) and the name of the table beginning in column twelve (12).  Each Livescan device will be responsible for ensuring that it is using the latest version of each table.

| File name | /(common partition)/valtabs/revcon.dta |
| --- | --- |
| Contents | Implement Date Time(yyyyjjjhhmm) ( Date Time(yyyyjjjhhmm) table name ( |
| Sample file | 19943321201 ( 19942551201ori.tbl ( 19933310001ofc.tbl ( 19941821201additional.tbl ( |

## B.10 	MESSAGE CODE TABLES

### Administrative Response Code– TABLE 11.1

| Type | Code |
| --- | --- |
| mad | A000: Resume transmission A010: Reaching input limit A020: Stop transmission A050: GTC queue is full A090: GTC shutting down (list may be expanded) |

### Accept Response Code - TABLE 11.2

| Type | Code |
| --- | --- |
| mac | 0000: Positive Response 0001: Negative Response (list may be expanded) |

### Reject Response Code - TABLE 11.3

| Type | Code |
| --- | --- |
| mrj | R001: NIST file inconsistent (not a NIST file) R002: NIST error R010: LEN not found R011: LEN invalid R012: TOT (Type1) not found R013: TOT (Type1) invalid R014: TCN (Type1) not found R015: Duplicate TCN (Type1) R016: TCN (Type1) invalid R120: EH segment not found R121: EH segment invalid R131: EHN segment invalid R140: ER2 segment not found R141: ER2 segment invalid R150: ER3 segment not found R151: ER3 segment invalid R160: ER4 segment not found R161: ER4 segment invalid R170: ER5 segment not found R171: ER5 segment invalid R200: Rejected at ERT by operator R201: Rejected at EDIT by operator R202: Rejected at IPC R203: Rejected at VV by operator R204: Rejected at VV2 by operator R205: Rejected at CV by operator R206: Rejected at PV by operator R207: Reject Palm Print R300: Critical Error R999: Fatal error (list may be expanded) |

## B.11 	MESSAGE EXAMPLES

The following message examples are actual messages retrieved from the Texas DPS GTC (with names and other identifying information changed).  They are plain text files.  In any place where an EAR segment is included in the message, the spaces included are part of the record.  The CCH Data Dictionary and the CCH Terminal Interface Specification define the EAR records and their layout.

### Administrative Messages

TO:        ALL
FROM:      NEC NATMS
SUBJECT:   mad
DATE/TIME: 1998/09/25 04:21:37
TYPE:      mad
CODE:      A090
LITERAL:   NATMS SHUTTING DOWN

TO:        ALL
FROM:      NEC NATMS
SUBJECT:   mad
DATE/TIME: 1998/09/25 04:52:53
TYPE:      mad
CODE:      A050
LITERAL:   NATMS QUEUE IS FULL

TO:        ALL
FROM:      NEC NATMS
SUBJECT:   mad
DATE/TIME: 1998/09/25 05:19:30
TYPE:      mad
CODE:      A000
LITERAL:   RESUME TRANSMISSION

### Acknowledgement Messages

TO:        002
FROM:      NEC NATMS
SUBJECT:   mac
DATE/TIME: 1998/09/25 00:42:04
TYPE:      mac
TCN:       41002069168
SAN:       0925980003
CODE:      0000
LITERAL:   Accepted by NATMS

### Reject Messages

TO:        042
FROM:      NEC NATMS
SUBJECT:   mrj
DATE/TIME: 1998/09/24 15:17:03
TYPE:      mrj
TCN:       41042000496
SAN:       0924980066
TRN:                 
RCODE:     R011
RLITERAL:  LEN invalid

TO:        002
FROM:      NEC NATMS
SUBJECT:   mrj
DATE/TIME: 1998/09/25 21:55:53
TYPE:      mrj
TCN:       41002069391
SAN:       0925980101
TRN:                 
RCODE:     R012
RLITERAL:  TOT(Type1) not found

TO:        038
FROM:      NEC NATMS
SUBJECT:   mrj
DATE/TIME: 1998/09/25 09:14:47
TYPE:      mrj
TCN:       41038044902
SAN:       0925980035
TRN:       9022073610
RCODE:     R015
RLITERAL:  Duplicate TCN(Type1)

TO:        027
FROM:      NEC NATMS
SUBJECT:   mrj
DATE/TIME: 1998/09/15 18:38:01
TYPE:      mrj
TCN:       41027063500
SAN:       0915980055
TRN:       9012139929
RCODE:     R200
RLITERAL:  Rejected at ERT by operator

TO:        002
FROM:      NEC NATMS
SUBJECT:   mrj
DATE/TIME: 1998/09/08  01:37:38
TYPE:      mrj
TCN:       41002066474
SAN:       
TRN:       901323867X
RCODE:     R201
RLITERAL:  Rejected at EDIT by operator

TO:        024
FROM:      NEC NATMS
SUBJECT:   mrj
DATE/TIME: 1998/09/19 21:41:50
TYPE:      mrj
TCN:       41024026029
SAN:       0919980124
RCODE:     R300
RLITERAL:  Critical Error
TRN:       901128433X
OCA:       982620955   
NAM:       SMITH,JOHANNA                 
MSG:*********************************************
MSG:  TRANSACTION WITH TRN = 901128433X
MSG:                   TCN = 41024026029
MSG:    ER2 SEGMENT 1
MSG:      Critical Err: Duplicate Error
MSG:        TRS  [A001]
MSG:*********************************************
SEG:ER2 X047719980919AFISFLORES             901128433X
09191998TX2460000          SMITH,JOHANNA          2345
OLD WEST ST(2.5 YRS)      ROUNDROCK           TX78681
9852960        982620955    A0010919199823990067
31.03(e)(2)(A) PCMB 205
09191998TX246013A
0000000000000000000010000000000000000000000000000000000000000000000000000000000000000000000000000000
MSG:*********************************************
MSG:  TRANSACTION WITH TRN = 901128433X
MSG:                   TCN = 41024026029
MSG:    ER2 SEGMENT 2
MSG:      Critical Err: Duplicate Error
MSG:        TRS  [A001]
MSG:*********************************************
SEG:ER2 X047719980919AFISFLORES             901128433X
09191998TX2460000          SMITH,JOHANNA          2345
OLD WEST ST(2.5 YRS)     ROUNDROCK           TX78681
9852960        982620955    A0010919199823990067
31.03(e)(2)(A) PCMB 205
09191998TX246013A
0000000000000000000010000000000000000000000000000000000000000000000000000000000000000000000000000000

### Identification Response Messages

TO:        038
FROM:      NEC NATMS
SUBJECT:   mid
DATE/TIME: 1998/09/24  16:12:19
TYPE:      mid
TCN:       41038044902
SAN:       
SID:       04337399
AGN:       31864
TRN:       9022073610
OCA:       9818540
NAM:       BREVINA,DEBI MARIA
SID:       04337399
FBI:                
FLG:        
HNH:       HIT
MSG:*********************************************
MSG:  TRANSACTION WITH TRN = 9022073610
MSG:                   TCN = 41038044902
MSG:  WAS IDENTIFIED AS
MSG:                   SID = 04339999        
MSG:*********************************************

TO:        015
FROM:      NEC NATMS
SUBJECT:   mid
DATE/TIME: 1998/09/23  18:18:53
TYPE:      mid
TCN:       41015074897
SAN:       
SID:       06134996
AGN:       85991
TRN:       9009185451
OCA:       85991
NAM:       BEDNOUR,DEBI MAE
SID:       06134996
FLG:       *
HNH:       NOHIT
MSG:*********************************************
MSG:  TRANSACTION WITH TRN = 9009185451
MSG:                   TCN = 41015074897
MSG:  WAS IDENTIFIED AS NEW
MSG:                   SID = 06139999
MSG:*********************************************

### Non-critical Error Messages

TO:        031
FROM:      NEC NATMS
SUBJECT:   mnc
DATE/TIME: 1998/09/25  01:45:47
TYPE:      mnc
TCN:       41031103299
SAN:       
SID:               
TRN:       9015259151
OCA:       JID118015   
NAM:       WILL,JOHN LOREN
MSG:*********************************************
MSG:  TRANSACTION WITH TRN = 9015259151
MSG:                   TCN = 41031103299
MSG:    ER2 SEGMENT 1
MSG:      Non Critical Err: Relation Check Error
MSG:        AD1[TRANSIENT                     ]
MSG:        CORRECTED AS [TRANSIENT                  ]
MSG:        ADC[ODESSA              ]
MSG:        CORRECTED AS [ODESSA              ]
MSG:        ADS[TX]
MSG:        CORRECTED AS [TX]
MSG:        ADZ[         ]
MSG:        CORRECTED AS [99999    ]
MSG:*********************************************
SEG:ER2  047719980925AFISRAMOS              9015259151
09241998TX0680200                    WILL,JOHN LOREN
TRANSIENT                     ODESSA              TX
70858          JID118015    A0010924199857070010
30.05(a) PC      MB 205
09251998TX068013A
0000000000111100000000000000000000000000000000000000000000000000000000000000000000000000000000000000
SGC:ER2  047719980925AFISRAMOS              9015259151
09241998TX0680200                    WILL,JOHN LOREN
TRANSIENT                  ODESSA              TX99999
70858          JID118015    A0010924199857070010
30.05(a) PC      MB 205
09251998TX068013A

TO:        007
FROM:      NEC NATMS
SUBJECT:   mnc
DATE/TIME: 1998/09/25  02:12:06
TYPE:      mnc
TCN:       41007023135
SAN:       
SID:               
TRN:       9017950048
OCA:       53619600    
NAM:       SMITH,JIMMIE DEAN
MSG:*********************************************
MSG:  TRANSACTION WITH TRN = 9017950048
MSG:                   TCN = 41007023135
MSG:    EH SEGMENT
MSG:      Non Critical Err: Relation Check Error
MSG:        OLT[  ]
MSG:        CORRECTED AS [XX]
MSG:        OLN[07286287                 ]
MSG:        CORRECTED AS [07286287                 ]
MSG:        OLS[TX]
MSG:        CORRECTED AS [TX]
MSG:*********************************************
SEG:EH   039619980925AFISSCHEET              TX0210000
SMITH,JIMMIE DEAN        MWKSUS12021963508180BLUBROLGT
07286287                 TX
N901795004853619600    0210100                      .
0000000000000000111000000000000000000000000000000000000000000000000000000000000000000000000000000000
SGC:EH   039619980925AFISSCHEET              TX0210000
SMITH,JIMMIE DEAN        MWKSUS12021963508180BLUBROLGT
XX07286287                 TX
N901795004853619600    TX0210100                    .
MSG:*********************************************
MSG:  TRANSACTION WITH TRN = 9017950048
MSG:                   TCN = 41007023135
MSG:    ER2 SEGMENT 1
MSG:      Non Critical Err: Not found in Table
MSG:        ORIA[0210100                      ]
MSG:        CORRECTED AS [TX0210100                  ]
MSG:      Non Critical Err: No data (mandatory)
MSG:        ANA[                              ]
MSG:        CORRECTED AS [SMITH,JIMMIE DEAN          ]
MSG:        ADN[   ]
MSG:        CORRECTED AS [215]
MSG:        REF[         ]
MSG:        CORRECTED AS [TX0210000]
MSG:*********************************************
SEG:ER2  047719980925AFISSCHEET             9017950048
092519980210100
53619600 A0010925199854040010DRIVING WHILE INTOXICATED
49.04            MA    HELD                   09251998
.
0000000011000000000000000101000000000000000000000000000000000000000000000000000000000000000000000000
SGC:ER2  047719980925AFISSCHEET             9017950048
09251998TX0210100                    SMITH,JIMMIE DEAN
53619600 A0010925199854040010DRIVING WHILE INTOXICATED
49.04            MA 215HELD
09251998TX0210000         .
MSG:*********************************************
MSG:  TRANSACTION WITH TRN = 9017950048
MSG:                   TCN = 41007023135
MSG:    ER2 SEGMENT 2
MSG:      Non Critical Err: Not found in Table
MSG:        ORIA[0210100                      ]
MSG:        CORRECTED AS [TX0210100                  ]
MSG:      Non Critical Err: No data (mandatory)
MSG:        ANA[                              ]
MSG:        CORRECTED AS [SMITH,JIMMIE DEAN          ]
MSG:*********************************************
SEG:ER2  047719980925AFISSCHEET             9017950048
092519980210100
53619600     A0020925199854050008DRIVING WHILE LIC SUSPEND
601.371(D)       M* 205HELD
09251998TX021013A         .
0000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000
SGC:ER2  047719980925AFISSCHEET             9017950048
09251998TX0210100                    SMITH,JIMMIE DEAN
53619600 A0020925199854050008DRIVING WHILE LIC SUSPEND
601.371(D)       M* 205HELD
09251998TX021013A         .

### Signal File (new submission)

SIGF:29134327.024
__END__

### LS Configuration File

/home/natms/tc/lsdir/nfs,1,10

### Validation Revision Control File

19983321201(
19982551201ori.tbl(
19983310001ofc.tbl(

### Tag 2.067 Examples

What follows are examples for the designation for tag 2.067.  More vendors will be added as they are defined.

#### NIST Type 2 Field 2.067

| Field Number | Identifier | Field Name | Character Type | Live Scan | Edit Criterion | Example | Special Characters |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2.067 | IMA | IMAGE CAPTURE EQUIPMENT, (Image Processing Field) LIVE SCAN MAKE, MODEL, SERIAL NUMBER | Alpha, Numeric, Special Character (A, N, S) | Generated | Single Occurrence MAKE (1-25) digits MODEL (1-25) digits SERIAL NUMBER (1-50) digits Separated by Unit Separator (US) | 2.067:DBI<US>1134<US>123456<GS> | Any printable 7-bit ASCII character is allowed. |

#### Live Scan Devices

| Live Scan Manufacturer | Manufacturer’s Specific Model | 2.067: MAKE Presentation | 2.067: MODEL Presentation (Sample) | 2.067: SERIAL NUMBER (Sample) | Example |
| --- | --- | --- | --- | --- | --- |
| Identix | Identix- TP600 | IDX | TP-600 | 12345 | 2.067:IDX<US> TP-600<US>12345 <GS> |
| Identix | Identix- TP2000 | IDX | TP-2000 | 12345 | 2.067:IDX<US> TP-2000<US> 12345<GS> |
| Identix (Formerly Visionics) | Visionics (DBI) Tenprinter Series S (1133S) | DBI | 1133S5 | 12345 | 2.067:DBI<US> 1133S5<US> 12345<GS> |
| Identix (Formerly Visionics) | Visionics (DBI) Tenprinter Series R (1133R) | DBI | 1133R5 | 12345 | 2.067:DBI<US> 1133R5<US> 12345<GS> |

Visionics Corporation and Digital Biometrics Inc. (DBI) merge to form the publicly traded Visionics Corporation.  As of June 26, 2002, Visionics Corporation has merged with Identix Incorporated (NASDAQ: IDNX).

#### High Volume Scanner Devices

| Live Scan Manufacturer | Manufacturer’s Specific Model | 2.067: MAKE Presentation | 2.067: MODEL Presentation (Sample) | 2.067: SERIAL NUMBER (Sample) | Example |
| --- | --- | --- | --- | --- | --- |
| TITAN-DBA | Titan DBA FC5000T | TSC | FC5000T | 12345 | 2.067:TSC<US>FC5000T <US>12345<GS> |
| TITAN-DBA | Titan DBA FC5000HS | TSC | FC5000HS | 12345 | 2.067:TSC<US>FC5000HS<US>12345<GS> |

#### Flat Bed Scanner Devices

| Live Scan Manufacturer | Manufacturer’s Specific Model | 2.067: MAKE Presentation | 2.067: MODEL Presentation (Sample) | 2.067: SERIAL NUMBER (Sample) | Example |
| --- | --- | --- | --- | --- | --- |
| TITAN-DBA | Titan DBA-FC500 | TSC | FC500 | 12345 | 2.067:TSC<US>FC500 <US>12345<GS> |
| AGFA | AGFA – T1200 | AGFA | T1200 | 12345 | 2.067:AGFA<US>T1200<US>12345<GS> |

# Appendix C — NIST Type 2 Definitions

| Tag | FBINam | DPSNam | Name | Who | EdtStr | SpcEdt | MinLen | MaxLen | MaxOcc |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1.01 | LEN | LEN | Record Length | FBI | n | 0 | 2 | 3 | 1 |
| 1.02 | VER | VER | Version | FBI | n | 0 | 4 | 4 | 1 |
| 1.03 | CNT | CNT | File Content | FBI | an | 0 | 9 | 48 | 1 |
| 1.04 | TOT | TOT | Type of Transaction | FBI | a | 0 | 3 | 5 | 1 |
| 1.05 | DAT | DAT | Date | FBI | n | 0 | 8 | 8 | 1 |
| 1.06 | PRY | PRY | Transaction Priority | FBI | n | 0 | 1 | 1 | 1 |
| 1.07 | DAI | DAI | Designation Agency ID | FBI | an | 0 | 9 | 9 | 1 |
| 1.08 | ORI | ORI | Originating Agency ID | FBI | an | 0 | 9 | 9 | 1 |
| 1.09 | TCN | TCN | Transaction Control Num | FBI | n | 0 | 10 | 40 | 1 |
| 1.10 | TCR | TCR | Transaction Control Ref | FBI | n | 0 | 10 | 40 | 1 |
| 1.11 | NSR | NSR | Native Scanning Resolution | FBI | n | 0 | 5 | 5 | 1 |
| 1.12 | NTR | NTR | Nominal Trans Resolution | FBI | n | 0 | 5 | 5 | 1 |
| 2.001 | LEN | LEN | Record Length | FBI | n | 0 | 2 | 5 | 1 |
| 2.002 | IDC | IDC | Image/Rec Designator | FBI | n | 0 | 2 | 2 | 1 |
| 2.005 | RET | RET | Retention Code | FBI | a | 0 | 1 | 1 | 1 |
| 2.006 | ATN | ATN | Attention Indicator | FBI | anb,$&-/()*; | 0 | 3 | 30 | 1 |
| 2.007 | SCO | SCO | Send Copy To | FBI | an | 0 | 9 | 19 | 9 |
| 2.009 | OCA | TRN* | Originating Ag Cas Num | FBI | an,-b/ | 0 | 1 | 10 | 1 |
| 2.014 | FBI | FBI | FBI Number | FBI | an | 0 | 1 | 9 | 5 |
| 2.015 | SID | SID | State ID Num | FBI | an | 0 | 3 | 10 | 5 |
| 2.016 | SOC | SOC | Social Security Number | FBI | n | 0 | 9 | 10 | 4 |
| 2.017 | MNU | MNU | Misc ID Number | FBI | an- | 0 | 4 | 15 | 4 |
| 2.018 | NAM | NAM | Name | FBI | a,-b | 0 | 3 | 30 | 1 |
| 2.019 | AKA | AKA | Aliases | FBI | a-&,b | 0 | 3 | 30 | 10 |
| 2.020 | POB | POB | Place of Birth | FBI | a | 0 | 2 | 2 | 1 |
| 2.021 | CTZ | CTZ | Country of Citizenship | FBI | a | 0 | 2 | 2 | 1 |
| 2.022 | DOB | DOB | Date of Birth | FBI | n- | 0 | 8 | 9 | 5 |
| 2.024 | SEX | SEX | Gender | FBI | a | 0 | 1 | 1 | 1 |
| 2.025 | RAC | RAC | Race | FBI | a | 0 | 1 | 1 | 1 |
| 2.026 | SMT | SMT | Scars, Marks, & Tattoos | FBI | ab | 0 | 3 | 10 | 10 |
| 2.027 | HGT | HGT | Height | FBI | an | 0 | 2 | 3 | 1 |
| 2.029 | WGT | WGT | Weight | FBI | n | 0 | 3 | 3 | 1 |
| 2.031 | EYE | EYE | Color Eyes | FBI | a | 0 | 3 | 3 | 1 |
| 2.032 | HAI | HAI | Hair Color | FBI | a | 0 | 3 | 3 | 1 |
| 2.033 | FPC | FPC | NCIC Fingerprint Class | FBI | an | 0 | 20 | 20 | 1 |
| 2.034 | PAT |  | Pattern Level Classification | FBI | an | 0 | 4 | 220 | 1 |
| 2.035 | PPA |  | Palm Prints Available | FBI | Y | 0 | 1 | 1 | 1 |
| 2.036 | PHT |  | Photo Available | FBI | Y | 0 | 1 | 1 | 1 |
| 2.038 | DPR |  | Date Printed | FBI | n | 0 | 8 | 8 | 1 |
| 2.039 | EAD |  | Employer & Address | FBI | an,b.&/-()# | 0 | 1 | 120 | 1 |
| 2.040 | OCP |  | Occupation | FBI | an,b.&/-()# | 0 | 1 | 50 | 1 |
| 2.041 | RES | AD1* | Residence | FBI | an,b.&/-# | 0 | 1 | 120 | 1 |
| 2.045 | DOA | DOA | Date of Arrest | FBI | n | 0 | 8 | 8 | 1 |
| 2.046 | DOS |  | Date of Arrest Suffix | FBI | a | 0 | 1 | 1 | 1 |
| 2.047 | ASL | AON* | Arrest Segment Literal | FBI | an,-&/#$.+b | 0 | 1 | 316 | 40 |
| 2.051 | CSL | * | Court Segment Literal | FBI | an,-&/#$b | 0 | 2 | 608 | 40 |
|  | CDD | CDD* | Court Disposition Date | FBI | an,-&/#$b | 0 | 8 | 8 | 1 |
|  | COL | * | Court Offense Literal | FBI | an,-&/#$b | 0 | 1 | 300 | 1 |
|  | CPL | * | Court Provision Literal | FBI | an,-&/#$b | 0 | 1 | 300 | 1 |
| 2.054 | SSD | SSD | Custody Start Date | FBI | n | 0 | 8 | 8 | 1 |
| 2.055 | SLE | * | Custody Literal | FBI | an,-&/#b | 0 | 1 | 300 | 1 |
| 2.056 | ICO |  | Identification Comments | FBI | an,-&/#b | 0 | 1 | 50 | 1 |
| 2.067 | IMA |  | Image Processing Field | FBI | an | 0 | 1 | 300 | 1 |
| 2.068 | IPP |  | Image Preprocessing | FBI | a | 0 | 1 | 1 | 1 |
| 2.070 | RAP |  | Request Elec RAP Sheet | FBI | a | 0 | 1 | 1 | 1 |
| 2.073 | CRI | ORIA | Arresting Agency ORI | FBI | an | 0 | 9 | 9 | 3 |
| 2.084 | AMP | AMP | Amputated or Bandaged | FBI | a | 0 | 0 | 60 | 9 |
|  | FGP |  | Finger Number | FBI | n | 0 | 2 | 2 | 1 |
|  | AMPCD |  | Amputated or Bandaged Code | FBI | a | 0 | 2 | 2 | 1 |
| 2.410 |  | EH | Identification | DPS | an | 1 | 396 | 396 | 1 |
| 2.411 |  | EHN | Identification Supplement | DPS | an |  | 358 | 358 | 12 |
| 2.412 |  | ER2 | Arrest Segment | DPS | an |  | 477 | 477 | 999 |
| 2.413 |  | SKN | Color of Skin | DPS | a |  | 3 | 3 | 1 |
| 2.414 |  | APC | AFIS Fingerprint Pattern | DPS | a |  | 10 | 10 | 1 |
| 2.415 |  | OLT | Operator License Type | DPS | a |  | 1 | 2 | 1 |
| 2.416 |  | OLN | Operator License Number | DPS | anlj |  | 1 | 25 | 1 |
| 2.417 |  | OLS | Operator License State | DPS | a |  | 2 | 2 | 1 |
| 2.418 |  | IDN | Identification Card Number | DPS | anlj |  | 1 | 25 | 1 |
| 2.419 |  | IDS | Identification Card State | DPS | a |  | 2 | 2 | 1 |
| 2.420 |  | ETH | Ethnicity | DPS | a |  | 1 | 1 | 1 |
| 2.421 |  | ORIA | ORI of Arresting Agency | DPS | anlj |  | 9 | 9 | 1 |
| 2.422 |  | TRS | Tracking Number Supplement | DPS | an |  | 4 | 4 | 999 |
| 2.423 |  | OCA | Local Case Number | DPS | an |  | 1 | 12 | 1 |
| 2.424 |  | ANA | Arrest Name | DPS | a |  | 3 | 30 | 1 |
| 2.425 |  | AGN | Local Agency Offender No. | DPS | anlj |  | 1 | 15 | 1 |
| 2.426 |  | GUN | Gun Indicator | DPS | a |  | 1 | 1 | 1 |
| 2.427 |  | DOO | Date of Offense | DPS | n |  | 8 | 8 | 999 |
| 2.428 |  | AON | Arrest Offense Numeric | DPS | n |  | 8 | 8 | 999 |
| 2.429 |  | AOL | Arrest Offense Literal | DPS | anlj |  | 1 | 46 | 999 |
| 2.430 |  | CIT | Statute Citation | DPS | anlj |  | 1 | 17 | 999 |
| 2.431 |  | LDA | Level & Degree of Offense | DPS | an |  | 2 | 2 | 999 |
| 2.432 |  | GOCA | General Offense Character | DPS | a |  | 0 | 1 | 999 |
| 2.433 |  | ADN | Arrest Disposition Numeric | DPS | a |  | 3 | 3 | 1 |
| 2.434 |  | ADD | Arrest Disposition Literal | DPS | anlj |  | 1 | 46 | 1 |
| 2.435 |  | ADA | Arrest Disposition Date | DPS | n |  | 8 | 8 | 1 |
| 2.436 |  | REF | Prosecutor ORI | DPS | anlj |  | 9 | 9 | 1 |
| 2.437 |  | JUV | Juvenile Indicator | DPS | a |  | 1 | 1 | 1 |
| 2.438 |  | SIDF | SID Flag | DPS | ans |  | 0 | 1 | 1 |
| 2.439 |  | ER3 | Prosecution Segment | DPS | an |  | 252 | 252 | 999 |
| 2.440 |  | ER4 | Court Disposition | DPS | an |  | 533 | 533 | 999 |
| 2.442 |  | ER5 | Custody/Supervision | DPS | an |  | 335 | 335 | 999 |

Table C1 — NIST Type 2 Definitions

## ER2 NOTES:

| TAG 2.041 | The FBI RES field is comprised of the Texas DPS AD1, ADC, ADS, and ADZ fields |
| --- | --- |
| TAG 2.047 | The FBI ASL field is comprised of the DOO subfield and the translation of the Texas AON field |

## ER4 NOTES:

| TAG 2.047 | The FBI ASL = DOA and translation of the CON from the ER4 segment |
| --- | --- |
| TAG 2.051 | The FBI CSL will consist of the FBI tags CDD COL and CPL. The data for these tags is defined as follows: CDD The CDD contained in the ER4 segment COL Translation of the CDN, translation of the CON and the LDC contained in the ER4 segment CPL "Confinement" & CMT, "Probation" & CPR and translation of the CPN contained in the ER4 segment |

## ER5 NOTES:

| TAG 2.047 | The FBI ASL = DOA and the NOM from the ER5 segment |
| --- | --- |
| TAG 2.055 | The FBI SLE will consist of the translation of the SSN and the SLE from the ER5 segment. |
| TAG 2.009 | The FBI OCA = AGN from the ER5 segment. |